## Slide 1: Design Challenge 2

## Slide 2
Each team will use 8 devices
There are one source device, one destination device, and six relay nodes. You need to transmit packets from the source device to the destination device.
You do not know the topology and we will make sure there is at least one route from the source to the destination
TAs will randomly turn on all devices (different from Design Challenge 1! )

## Slide 3
D
Des
E
B
A
F
C
Src
A
C
means A can communicate with C
Example
Broadcast

## Slide 4
D
Des
E
B
A
F
C
Src
Source sends packet P1 periodically
P1
P1
P1
P1
P1

## Slide 5
D
Des
E
B
A
F
C
Src
Destination sends ACKs to the Source
ACK(P1)
ACK(P1)
ACK(P1)
ACK(P1)

## Slide 6
D
Des
E
B
A
F
C
Src
After Source receives the ACK,
it will stop and sends packet P2 periodically
P2
P2
P2
P2
P2

## Slide 7
TAs will prepare the code of the source device(you cannot change the code)
The source device will do :
Continuously sends the packet that sequence number is 0x00
While receives the ACK of the packet with the sequence number 0x00, continuously sends the packet that sequence number is 0x01
.........
When source receives the ACK of the packet with the sequence number 0x13, your demo complete

## Slide 8
The code of the destination device you need to write yourself
The destination device will do :
Wait for packet with sequence number 0x00 from source device
While receives the packet with sequence number 0x00, sends ACKs with sequence number 0x00 to the source device and print the payload of the received packet on the terminal
………….
While receives the packet with sequence number 0x13, sends ACKs with sequence number 0x13 to the source device and print the payload of the received packet on the terminal
Finish!!

## Slide 9: Packet format
Byte-0 | Byte-1 | Byte-2 | Byte-3 | Byte-4
Header | Header | Sequence | isACK | Payload
0x05 | 0x30 | 0x00~0x13 | 0x00 or 0x01 | ???
This is the payload of the packet that transmitted by the source device
Sequence : the packet is on the nth round (0x00 means the first round)
isACK :
  0 means the packet from source
  1 means the packet from destination(ACK)
Payload :
  The data we define (on demo)
  You can put anything when you are testing, but you can not know the payload until demo

## Slide 10
For example :
Source device continuously sends the packet
Source device receives the ACK from destination device
Source device continuously sends the packet
Byte-0 | Byte-1 | Byte-2 | Byte-3 | Byte-4
Header | Header | Sequence | isACK | Payload
0x05 | 0x30 | 0x00 | 0x00 | 0x0A
Byte-0 | Byte-1 | Byte-2 | Byte-3 | Byte-4
Header | Header | Sequence | isACK | Payload
0x05 | 0x30 | 0x00 | 0x01 | 0x0A
Byte-0 | Byte-1 | Byte-2 | Byte-3 | Byte-4
Header | Header | Sequence | isACK | Payload
0x05 | 0x30 | 0x01 | 0x00 | 0x0B

## Slide 11: Grading
Source device will send packets with sequence number from 0x00~0x13, if the destination device receives packets with sequence number
  0x00~0x04, you will get 70%
  0x00~0x09, you will get 75%
  0x00~0x0D, you will get 80%
  0x00~0x13, you will get 85%
You have only 5 minutes to transmit all packets (0x00~0x13).
If the time interval that destination device receives the packer from 0x00~0x13 is more short, you get higher score
  The 1st group get 90%
  …….
  The 5th group get 86%
Report(10%)

## Slide 12: Challenge
We will turn off one relay node after destination receives the packet with sequence 0x0E, this means that your protocol must dynamically adjust the route
We will make sure there is still at least one route from the source to the destination
Hints:
You can use 1) “flooding” or 2) create routing tables or 3) try to generate “IDs” for each device and use your protocol in the Design Challenge 1